## Slide 1: Hydraulic calculations

## Slide 2: Understanding Hydraulics
Most important aspect of hydraulics is pressure
Pressure in whole systems is the same

## Slide 3
Pressure

## Slide 4: Formula
WHERE…

## Slide 5: Formula units
Pascal (Pa)
Newton (N)
Square Meters (m²)

## Slide 6: Calculating Area
OR

## Slide 7: Pressure in hydraulics
=

## Slide 8
Force 1
Force 2
Area 1
Area 2

## Slide 9: example
A diagrammatical representation of a hydraulic press is shown.
The applied force on piston A is 0,85 kN. The diameter of piston A is 36 mm and the diameter of piston B is 225 mm.

## Slide 10
Calculate the pressure in the system.
Calculater the force Piston B can lift

## Slide 11: Solution
Apply formula
Have only 1 variable…
First calculate area … ALWAYS CONVERT TO METERS!!!
So … 36mm = 0,036m

## Slide 12: Calculating Area
0,001017876 m

## Slide 13: Calculating pressure
835072,2485Pa
835,07 kPa

## Slide 14: Calculation force on piston b
Apply formula
Have only 1 variable…
First calculate area … ALWAYS CONVERT TO METERS!!!
So … 225mm = 0,225m

## Slide 15: Calculating Area
0,039760782 m

## Slide 16
Therefore:
Force = Pressure x Area
Force = 835072,2485 x 0,039760782
Force = 33209,00287 N
Force = 33,21 kN

## Slide 17: ?