## Slide 1: SYSTEM OF FORCES
Danie van der Westhuizen
SES: Mechanical Technology

## Slide 2: CARTESIAN PLANE
0°
90°
180°
270°

## Slide 3: QUADRANTS

## Slide 4: Example

## Slide 5: Note !!
ALL forces need to be PULLING forces.
First convert all pushing forces into PULLING forces, BEFORE calculating angles.
THUS:
Convert to pulling force

## Slide 7: Calculating angles of forces

## Slide 8: Calculate Arithmetic Sum
Force | Vertical component |  | Horizontal component | 
60N | Y = 60 sin 0° | 0N | X = 60 cos 0° | 60N
130N | Y = 130 sin 220° | -83,56N | X = 130 cos 220° | -99,59N
75N | Y = 75 sin 90° | 75N | X = 75 cos 90° | 0N
50N | Y = 50 sin 125° | 41,96N | X = 50 cos 125° | -28,68N
Total: |  | 32,40N | Total | -68,27N

## Slide 9: First plot on Cartesian plane
R

## Slide 10: Resultant by using Phythagoras
R² = x² + y²
= (-68,27)² + (32,4)²
= 4656,70 + 1049,76
=
= 75,57N

## Slide 11: Direction of Resultant
Determining the direction, you must understand the compass

## Slide 12: Bearings on a compass

## Slide 13: Now apply compass to Cartesian plane

## Slide 14: First plot on Cartesian plane
R
N
W
S
E

## Slide 15: Calculate the direction of Resultant
Tanθ =
=
Tanθ = 2,11
= 64,64°
The resultant has a magnitude of 75,54N in the direction of 64,64° West from North
or
at a bearing of 295,36°

## Slide 16: Questions ??

## Slide 17: Thank You